Hazard Analysis

Work Plan Title:	Reference of magnets @ Industrial Bldg. 2

Date: 30, May 2007

Prepared By:	 G.Crutcher, C. Wilson

Reviewed By: (G. Coppola)

Approved By (Supervisor/Task Manager): B. Oshinowo, G. Coppola

Description of work:

Reference of magnets at IB2, (physical centerline to fiducials)

Personal Protective Equipment:  (Check protective equipment required for the job.)

X Safety glasses     □ Side shields	□ Chemical splash goggles

X Hearing Protection (as needed)	□ Hard Hats

□ 3.0 Braising goggles	□ Impact goggles

□ Face shield	□ Rubber apron

□ Leather gloves	□ Hot/Cold thermal protective gloves

□ Chemical resistant gloves (specify type):	□ Respirators

□ Other required PPE (specify): 	□ Fall protection equipment (specify):

Equipment required for the job:  (List the tools needed to perform the job.)

API laser-tracker, tracker cart, and accessories (prisms, small and standard), Lap-top computer, magnets inserts for the fiducials, 5 minute epoxy, letter punches and Brother Label-Maker for marking fiducial names, extension power cord,

Work Plan History Information:  (List any lessons learned accidents from this job, tips from previous jobs)

Make sure magnet to be referenced to on a SOLID and STABLE SURFACE.

# HAZARD ANALYSIS

| Step | Description | Hazards | Precautions / Safety Procedures |
| --- | --- | --- | --- |
| 1 | Possibility for Eye Injury | Machining or grinding in the general area, stamping fiducial names. | Wear safety glasses |
| 2 | Hearing Loss | Loud noises from the production floor | Use Hearing Protection as needed |
| 3 | Residual Radioactivity | These magnets have been exposed to a beam line environment | Must wear TLD, (film-badge), and pocket dosimeter |
| 4 | Trip hazards | Extension cords, air-lines, pallets, materials stored on floor | Use caution (note location of items on floor) |
| 5 | Overhead cranes, fork-lifts, and hoists | Bodily injury, or equipment damaged from craned items | Be aware of crane, hoists, and fork-lift activity, use in area |
| 6 |  |  |  |
| 7 |  |  |  |
| 8 |  |  |  |
| 9 |  |  |  |
| 10 |  |  |  |

(Use additional pages as needed.)

My supervisor has reviewed this hazard analysis with me and I understand the hazards and required precautionary actions.  I will follow the requirements of this hazard analysis or notify my supervisor if I am unable to do so.  I understand that there are Environmental, Safety and Health Professionals on staff if I need further assistance or clarification.

| Name and ID (please print) | Signature | Date |
| --- | --- | --- |