Hazard Analysis

Work Plan Title: Vertical Control Upgrade 2008

Date:  21 May 2008

Prepared By:	 M. O’Boyle, G. Crutcher, C. Bradford, and R. Wyatt

Reviewed By: Gary Coppola

Approved By (Supervisor/Task Manager): John Kyle

Description of work:

Site wide elevation runs to update vertical control network.

Personal Protective Equipment:  (Check protective equipment required for the job.)

X Safety glasses     □ Side shields	□ Chemical splash goggles

□ Hearing Protection	□ Hard Hats

□ 3.0 Braising goggles	□ Impact goggles

□ Face shield	□ Rubber apron

X Leather gloves	□ Hot/Cold thermal protective gloves

□ Chemical resistant gloves (specify type):	□ Respirators

X Other required PPE (specify): 	□ Fall protection equipment (specify):

Insect repellent, appropriate clothing i.e. boots, long pants, hats, for the outside fieldwork portion.

Safety vest and signs if on roadways.

Cell-phones for emergency contact

Equipment required for the job:  (List the tools needed to perform the job.)

DNA03 automatic level with extra battery

Two 2-meter level rods.

PK nails, turning pins, >7 kg turtles, hammer, (safety glasses when using hammer.)

18” Rebar for permanent turning points.

Umbrella

Tripod

Flags and Stop/Slow signs (when on well traveled roads)

Work Plan History Information:  (List any lessons learned accidents from this job, tips from previous jobs)

Dig permit/waiver required for installation of permanent traverse points. Contact   person is Carl Holmgren, FESS, at extension 3174 or extension 5000.

Set rebar flush or below grade to avoid trip hazards.

Remove PK nails after elevation run.

# HAZARD ANALYSIS

| Step | Description | Hazards | Precautions / Safety Procedures |
| --- | --- | --- | --- |
| 1 | Trip Hazards | Possible holes and irregular ground. Branches and debris. | Walk cautiously through fields Wear high top boots with ankle support. |
| 2 | Insects | Flies, Mosquitoes, Ticks Bees, Wasps | Use insect spray Look for Ticks on body after each session. |
| 3 | Weather | Lightning Rain Heat Cold | Do not work in heavy rain, snow, hail or when lightning is present. Wear appropriate clothing. Water breaks, cooling / warming breaks as needed, sun block. |
| 4 | Plants | Poisonous | Beware of the plants i.e. poison ivy, poison oak. Learn what they look like and avoid them. Wear long pants, long sleeved shirts. |
| 5 | Animals | Snakes Nesting Birds Coyotes | Be observant and try to stay away from them when possible |
| 6 | Remote area | Accidents such as falls cuts and bites or stings. | Cell phone or some kind of electronic communication device. At least 2 people within hearing range of each other. |
| 7 | Traffic | Accidents | All personnel must wear safety vest. Signs must be used along with flagmen if needed. |
| 8 | Setting Permanent Points | Eye and Hand injuries Hitting Utilities Trip Hazard | Safety glasses Leather gloves Dig Permit or Wavier must be acquired prior to the installation of points Set rebar flush or below grade |

(Use additional pages as needed.)

My supervisor has reviewed this hazard analysis with me and I understand the hazards and required precautionary actions.  I will follow the requirements of this hazard analysis or notify my supervisor if I am unable to do so.  I understand that there are Environmental, Safety and Health Professionals on staff if I need further assistance or clarification.

| Name and ID (please print) | Signature | Date |
| --- | --- | --- |

Contacts:

HOLMGREN, CARL L

COPPOLA, GARY H

KYLE, JOHN C.