Hazard Analysis

Work Plan Title: Horizontal Locations for Vertical Control Upgrade 2008

Date:  21 May 2008

Prepared By:	 M. O’Boyle, G. Crutcher, C. Bradford, and R. Wyatt

Reviewed By:  Gary Coppola

Approved By (Supervisor/Task Manager): John Kyle

Description of work:

Obtain Geodimeter coordinates on permanent vertical control points.

Personal Protective Equipment:  (Check protective equipment required for the job.)

X Safety glasses     □ Side shields	□ Chemical splash goggles

□ Hearing Protection	□ Hard Hats

□ 3.0 Braising goggles	□ Impact goggles

□ Face shield	□ Rubber apron

X Leather gloves	□ Hot/Cold thermal protective gloves

□ Chemical resistant gloves (specify type):	□ Respirators

X Other PPE (specify): 	□ Fall protection equipment (specify):

Insect repellent, appropriate clothing i.e. boots, long pants, hats, for the outside fieldwork portion as needed.

Safety vest and signs if on roadways.

Cell-phones for emergency contact

Equipment required for the job:  (List the tools needed to perform the job.)

Geodimeter with batteries

Tripods

Prisms, prism pole, target kits

Flags and Stop/Slow signs (when on well traveled roads)

18” Rebar

Hammer (safety glasses when using hammer)

Work Plan History Information:  (List any lessons learned accidents from this job, tips from previous jobs)

Dig permit/waiver required for installation of permanent traverse points. Contact person is Carl Holmgren, FESS, at extension 3174 or extension 5000.

Set rebar flush or below grade to avoid trip hazards.

# HAZARD ANALYSIS

| Step | Description | Hazards | Precautions / Safety Procedures |
| --- | --- | --- | --- |
| 1 | Trip Hazards | Possible holes and irregular ground. Branches and debris. | Walk cautiously through fields Wear high top boots with ankle support. |
| 2 | Insects | Flies, Mosquitoes, Ticks Bees, Wasps | Use insect spray Look for Ticks on body after each session. |
| 3 | Weather | Lightning Rain Heat Cold | Do not work in heavy rain, snow, hail or when lightning is present. Wear appropriate clothing. Water breaks, cooling / warming breaks as needed, sun block. |
| 4 | Plants | Poisonous | Beware of the plants i.e. poison ivy, poison oak. Learn what they look like and avoid them. Wear long pants, long sleeved shirts. |
| 5 | Animals | Snakes Nesting Birds Coyotes | Be observant and try to stay away from them when possible |
| 6 | Remote area | Accidents such as falls cuts and bites or stings. | Cell phone or some kind of electronic communication device. At least 2 people within hearing range of each other. |
| 7 | Traffic | Accidents | All personnel must wear safety vest. Signs must be used along with flagmen if needed. |
| 8 | Setting Permanent Points | Eye and Hand injuries Hitting Utilities Trip Hazard | Safety glasses Leather gloves Dig Permit or Wavier must be acquired prior to the installation of points Set rebar flush or below grade |

My supervisor has reviewed this hazard analysis with me and I understand the hazards and required precautionary actions.  I will follow the requirements of this hazard analysis or notify my supervisor if I am unable to do so.  I understand that there are Environmental, Safety and Health Professionals on staff if I need further assistance or clarification.

| Name and ID (please print) | Signature | Date |
| --- | --- | --- |

Contacts:

HOLMGREN, CARL L

COPPOLA, GARY H

KYLE, JOHN C.