Hazard Analysis

Work Plan Title:	NuMI beamline in the MI Stub area

Date:  02, April, 2008

Prepared By:	 Gary W. Crutcher

Reviewed By: (optional) Virgil Bocean

Approved By (Supervisor/Task Manager):  Gary Coppola

Description of work:  As-found / As-set alignment surveys of  magnets and other devices  in NuMI beamline	 in the MI Stub area.

Personal Protective Equipment:  (Check protective equipment required for the job.)

□ Safety glasses     □ Side shields	□ Chemical splash goggles

“X” Hearing Protection	“X” Hard Hats

□ 3.0 Braising goggles	□ Impact goggles

□ Face shield	□ Rubber apron

□ Leather gloves	□ Hot/Cold thermal protective gloves

□ Chemical resistant gloves (specify type):	□ Respirators

□ Other required PPE (specify): 	“X” Fall protection equipment (specify):

Equipment required for the job:

API Laser Tracker, Laptop Computer, Tracker Fixtures (i.e. prisms, nests, tripods / stands, etc.), two each flash-lights, canned air for cleaning control points and fiducials.

Also obtain copies of needed control files, magnet references, and beam-sheets.  Have all the appropriate tools needed for alignment.

Work Plan History Information:

Obtain Keys from control room, sign / date RWP’s, move equipment into the tunnel with adequate time for the tracker to acclimate if possible.

# HAZARD ANALYSIS

| Step | Description | Hazards | Precautions / Safety Procedures |
| --- | --- | --- | --- |
| 1 | Fall Protection | Falling from elevated catwalks (platform) or ladders or in tunnel. Beware of existing ledges in the tunnel. May have had the railing removed for magnet installation. | Use harness if necessary or required and tie-of the monorail. Must ware a harness if working on catwalks (upper platforms) or off girders. If ladders are used in some situations, tie-off ladder, or use a buddy to secure as necessary. |
| 2 | Trip Hazards | Tripping over equipment, extension cords, or materials stored on floor | Walk cautiously and be aware of your surroundings. Clear work area of unnecessary items as needed. |
| 3 | Loud Noises | Hearing damage caused by excessive noise, from machinery, water lines, and fans. | Carry ear protection with you and use as needed. |
| 4 | Head Injuries | Material falling | Hard Hats to be worn whenever anyone is working overhead, or any cranes are in operation in the area. |
| 5 | Back / Body Injury | Back or body injury caused from lifting too much weight or improper lifting technique | Use proper lifting technique, do not place your body in awkward positions while lifting, Utilize a buddy while lifting excessive weight or moving ladders or heavy equipment. |
| 6 | Slope of Magnets in Tunnel | Magnet slipping off of stands | Be aware of the fact that the magnets in much of the extraction line are on as much as 15.8% slope / grade. Make sure that the magnets feet are resting in the cups of the stands. |
| 7 | Exposure to heat | Prolonged exposure to excessive heat in tunnel | This area is prone to having excessive heat with no access to water or a cooler climate. Take water breaks as needed, and move to a cooler atmosphere for breaks as needed. |
| 8 |  |  |  |
| 9 |  |  |  |
| 10 |  |  |  |

(Use additional pages as needed.)

My supervisor has reviewed this hazard analysis with me and I understand the hazards and required precautionary actions.  I will follow the requirements of this hazard analysis or notify my supervisor if I am unable to do so.  I understand that there are Environmental, Safety and Health Professionals on staff if I need further assistance or clarification.

| Name and ID (please print) | Signature | Date |
| --- | --- | --- |