Hazard Analysis

Work Plan Title: Obtain X, Y, and Z coordinates on monitoring wells/Piezometers

Date:  4, June 2007

Prepared By:	 R.L. Wyatt

Reviewed By:(Gary Coppola)

Approved By (Supervisor/Task Manager): Gary Coppola

Description of work:

- Using GPS Rover to obtain X and Y coordinates on 109 wells on site.

- Using the DNA03 automatic level and 2 meter rods to obtain the elevation.

Personal Protective Equipment:  (Check protective equipment required for the job.)

X Safety glasses     □ Side shields	□ Chemical splash goggles

□ Hearing Protection	□ Hard Hats

□ 3.0 Braising goggles	□ Impact goggles

□ Face shield	□ Rubber apron

□ Leather gloves	□ Hot/Cold thermal protective gloves

□ Chemical resistant gloves (specify type):	□ Respirators

X Other required PPE (specify): 	□ Fall protection equipment (specify):

Insect repellent, appropriate clothing i.e. boots, long pants, hats, for the outside fieldwork portion. Safety vest and signs if on roadways

Equipment required for the job:  (List the tools needed to perform the job.)

Location site map of 109 wells

GPS Rover with extra battery (Jim Niehoff)

DNA03 automatic level with extra battery

Two 2-meter level rods

PK nails/turning pins, hammer  (safety glasses when setting pins.)

Work Plan History Information:  (List any lessons learned accidents from this job, tips from previous jobs)

Using site map, locate wells to obtain an X, Y, and H coordinate.  Dig permits may be required. Use of any chemicals around well site prohibited. (Wasp spray, paint, etc.)

# HAZARD ANALYSIS

| Step | Description | Hazards | Precautions / Safety Procedures |
| --- | --- | --- | --- |
| 1 | Trip Hazards | Possible holes and irregular ground. Branches and debris. | Walk cautiously through fields Wear high top boots with ankle support. |
| 2 | Insects | Flies, Mosquitoes, Ticks Bees, Wasps | Use insect spray Look for Ticks on body after each session. |
| 3 | Weather | Lightning Rain Heat Cold | Do not work in heavy rain or when lightning is present. Wear appropriate clothing. Water breaks, cooling / warming breaks as needed, sun block. |
| 4 | Plants | Poisonous | Beware of the plants i.e. poison ivy, poison oak. Learn what they look like and avoid them. Wear long pants, long sleeved shirts. |
| 5 | Animals | Snakes Nesting Birds | Be observant and try to stay away from them when possible |
| 6 | Remote area | Accidents such as falls cuts and bites or stings. | Cell phone or some kind of electronic communication device. At least 2 people within hearing range of each other. |
| 7 | Traffic | Accidents | All personnel must wear safety vest. Signs must be used along with a flagman if needed. |
| 8 |  |  |  |
| 9 |  |  |  |
| 10 |  |  |  |

(Use additional pages as needed.)

My supervisor has reviewed this hazard analysis with me and I understand the hazards and required precautionary actions.  I will follow the requirements of this hazard analysis or notify my supervisor if I am unable to do so.  I understand that there are Environmental, Safety and Health Professionals on staff if I need further assistance or clarification.

| Name and ID (please print) | Signature | Date |
| --- | --- | --- |