## Slide 1: HL-LHC Tracking Trigger Challenges  the view from science and technology
Ted Liu (FNAL)
APS meeting,
April 7th, 2014
Originally assigned title: “New Trigger Architectures”

## Slide 2: Some colliders in the past
Quarks
Leptons
Force
Carriers
KLOE/DAΦNE
MARK/SPEAR,
BES/BEPC
CLEO/CESR,
Argus/DORIS
BaBar/PEP-II,
Belle/KEK-B
…
SLD/SLC,
(Aleph,Delphi,Opal,L3)/LEP
AdA,
VEPP,
ACO,
ADONE, CEA
…
(AMY,TOPAZ,
VENUS)/TRISTAN
(JADE,MARK J,
PLUTO, TASSO)/PETRA
ep (H1, ZEUS, HERMES, HERA-B) /HERA
pp-bar (UA1, UA2)/SppS, (CDF,D0)/Tevatron
pp (Atlas, CMS, ALICE, LHCb)/LHC
Trigger challenges at high luminosity:
e+e-, ep colliders: beam background
pp-bar, pp colliders: pile up & pile up

## Slide 3
Fermilab site
Lake
Michigan
Chicago
In the Near Future:
High Luminosity LHC

## Slide 4: Rate = s L
With LHC design luminosity of 1034cm-2s-1 = 10 nb-1s-1 = 10-2 pb-1s-1, at 14 TeV:
  s (top pair production) ~ 700 pb  ~ 7 Hz
  s (inelastic scattering) ~ 70 mb  ~700 MHz
Actual event rate is limited by bunch crossing
at 20/40MHz, this leads to:
    Multiple interactions per beam crossing (pile up)
    At HL-LHC, expect ~ 140 – 200 pile up.

## Slide 5
HZZ  ee, MH= 300 GeV for different luminosities in CMS
1032 cm-2s-1
1033 cm-2s-1
1034 cm-2s-1
1035 cm-2s-1
Pile up vs luminosity
HL-LHC

## Slide 6: Expected Pile-up at High Lumi LHC in ATLAS at 1035
Nch(|y|0.5)

## Slide 7: ATLAS and CMS only have calorimeter and muon trigger at Level 1 (no tracking trigger available)
Complexity handled in software on CPUs
at high level trigger (HLT)
The approach works well only at lower luminosity …
At HL-LHC, will need to move some of HLT algorithms into L1.
Key extra info: silicon based tracking at L1.
Easier said then done.

## Slide 8
Silicon based tracking trigger at L1 will be crucial for trigger objects reconstruction at
higher luminosity:
Electron
Photon
Muon
Tau
Jets
b-jets
missing ET
….
Essential for establishing
nature of EWSB,
new physics …
Pileup at HL-HC: > ~ 140 (only 20 shown here)
real event
Impact of track reconstruction at L1

## Slide 9
CMS L1 Tracking Trigger:
Will need to reconstruct charged particle trajectories “on-the-fly” for every beam crossing (25 ns, or 40 Million beam crossings per second), from an ocean of input data (bandwidth required to transfer up to ~ 50-100Tb/s)
This requires extremely
fast high bandwidth data communication as well as massive pattern recognition power,
with lots known patterns to be compared against the multiple input data streams simultaneously with near zero latency (~ few μs)
This is challenging!
Pileup at HL-HC: > ~ 140 (only 20 shown here)
Impact of track reconstruction at L1

## Slide 10: High Performance Computing  from US “Report to the President and Congress” by President’s Council of Advisors on Science and Technology, Dec. 2010 (page 65)
Compute-intensive
  massively parallel computation involving very large number of processing elements;
Communication-intensive
  high-speed transfer of data among processing elements;
Data-intensive
  high-speed manipulation of very large quantities of data
HL-LHC L1 Tracking Trigger is High Performance Computing
(Non-von Neumann approach)
but with very Low Latency and in Real Time
HL-LHC requires the most advanced Real Time processing technology

## Slide 11: The LHC case
Frontier physics at LHC in the future:
Go to Higher Energy: needs more aggressive R&D in Magnet
OR
Go to Higher Luminosity: needs aggressive Tracking Trigger R&D
It has become clear that track based trigger capability will be crucial to the frontier physics reach at LHC in the future, as luminosity increases.
The current technology using fiber data transfer, FPGAs, custom chips and modern PCs cannot be scaled in a simple manner to accommodate all the tracking trigger demands.
Significant improvements, or breakthroughs, will be needed. In other words, aggressive R&D efforts will be required.
The rest of talk will show a few examples of the challenges and
 How to take advantages of modern (new/emerging) technologies

## Slide 12
CDF SVXII
Data formatting
Pattern Recognition
Track
Fitting
Data transfer
HLT
Detector design for triggering
Beam spot
FPGA vs GPU vs CPU
Silicon Based Tracking Trigger at Hadron Colliders
Partition detector into
trigger towers/sectors
Pick your favorite method:
Associative Memory (AM) Approach
(proven approach from CDF/SVT)
Hough Transformation
tracklet-based
Adaptive Pattern Recognition
Biology Inspired …
your choice here…
Finer pattern recognition
Will use Associative Memory approach
as an example in this talk
Based on Content Addressable Memory

## Slide 13: Content Addressable Memory (CAM)
CAM Operation
  user supplies a data word and it searches its entire memory in a single operation to see if that data word is stored anywhere in it
One incoming pattern/hit at a time
There is no memory of previous matches
Pattern 1
Pattern 1
Match
Pattern 3
Pattern 3
Match
Match
Pattern 7
Pattern 7
Match
…..

## Slide 14: The AM approach
Pattern Recognition Associative Memory (for HEP)
  Based on CAM cells to match and majority logic to associate hits in different detector layers to a set of pre-determined hit patterns (simple working unit, yet massively parallel)
  Pattern Recognition finishes right after all hits arrive
  A PR engine naturally handles a given detector region: divide & conquer
Layer 1
Address 4
Match
Layer 1
Address 4
Match
Match
Layer 3
Address 7
Match
Match
Layer 3
Address 7
Match
Match
Match
Match
Layer 3
Address 9
Match
Match
Match
Match
Layer 3
Address 9
Match
Match
Match
Match
Match
Match
Match
Match
Layer 2
Address 1
Match
Match
Match
Match
Layer 2
Address 1
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Layer 4
Address 4
Match
Match
Match
Match
Match
Match
Layer 4
Address 4
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Layer 2
Address 4
Match
Match
Match
Match
Match
Match
Match
Match
Match
Layer 2
Address 4
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Road!
CAMs
Linearized track fitting can follow each road found (FPGA implementation)
Animation by Jim Hoff (FNAL engineer)
…….
Millions of
Patterns
compared
at the same
time

## Slide 15
Roads
Find low resolution track candidates called “roads”.
Then fit tracks inside roads.
a linear approximation gives near ideal precision
Super Bin (SB)
Tracking in 2 steps
Pattern recognition and track fitting done separately and pipelined
A very successful approach at CDF for RunII, based on
Associative Memory, which in turn, based on CAM (Content Addressable Memory)
Parallel processing,
avoiding the typical power law dependence of
execution time on occupancy and
solving the pattern recognition in times roughly proportional to the number of hits.

## Slide 16
2 meters
0,1
2,3
4,5
6,7
8,9
10,11
fan-out
fan-in
CDF original SVT system had ~400K patterns total …
128 patterns per AMchip -- commissioned around ~2001
(initial concept started in middle 80s!)
Question: can one integrate all these into one chip for HL-LHC?

## Slide 17: A sense of scale: Atlas Silicon Tracker vs CDF SVX II
Total # of readout channels:
PIXELS: 80 millions
SCT: 6 millions
Channels used for SVT:
~ 0.2 millions
CDF SVX II
Other relevant aspects:
Collision energy/rate
Pileups/occupancy
Materials
Cabling mapping
…
FTK AM Patterns desired: ~1 Billion patterns 1st used: ~400K

## Slide 18
CDF SVXII
Data formatting
Pattern Recognition
Track
Fitting
Data transfer
HLT
Detector design for triggering
Beam spot
Silicon Based Tracking Trigger at Hadron Colliders
Partition detector into
trigger towers/sectors
Pick your favorite method:
Associative Memory (AM) Approach
(proven approach from CDF/SVT)
Hough Transformation
tracklet-based
Adaptive Pattern Recognition
Biology Inspired …
your choice here…
Finer pattern recognition
Need massive parallelism and to process in parallel different
regions of the detector for the same crossing (regional multiplexing, L1&L2),
and different crossings coming at different times (time multiplexing, L1)
Requires high bandwidth, low latency, and flexible real time communication,
and a full mesh backplane based hardware platform is a natural fit.
(solution: take advantage of the technology developed from telecommunication industry)

## Slide 19
Input data from all silicon detector modules has to
be formatted into 64 η-φ trigger towers after
reformatting and sharing, ready for downstream
pattern recognition
4 in η
First take a look at: Data formatting challenges for Atlas FTK at L2
The existing silicon tracker was not
designed for tracking trigger …

## Slide 20
3D paper models at Fermilab with detailed ROD ID mapping, to
help understanding the issues
FTK Data Formatting Challenges
By Yasu Okumura

## Slide 21
Atlas FTK 64 Trigger Towers (TT) data sharing needs
Detailed beam data analysis using exact module/ROD cable mapping to trigger towers
64 TT
64 TT

## Slide 22: Data sharing/switching techniques
Traditional data sharing
Data sharing with ATCA
  high speed full-mesh backplane
  ~ 40-100 Gbps point to point
Advanced
Telecommunication
Computing
Architecture

## Slide 23
How to use ATCA backplane for data sharing
(1 FPGA per trigger tower, 2 trigger towers per board,
32 boards needed over 4 ATCA shelves)
ATCA
Full-mesh
backplane
Only data sharing links shown, not inputs/outputs
Fermilab (2011)
Data Formatter
Concept:
ATCA-based

## Slide 24
From “Data Formatter Design Specification”, Fermilab-TM-2553-E-PPD, page 78.
Available at: http://www-ppd.fnal.gov/EEDOffice-w/Projects/ATCA/
The band would be much cleaner without ROD constraints:
(useful to guide new tracker design for trigger)

## Slide 25
ATCA
CMS
Tracking Trigger Towers
For simplicity, let’s assume one crate is assigned to one trigger tower

## Slide 26: CMS: Module design vs Tracker design vs Trigger processing
Back-end
Off-detector
Track Finding
stubs
Module Design Tracker Design Track Finding
CMS new tracker design
~15K modules involved
Working assumptions:
~15K fibers to trigger,
3.2Gbps payload each,
~ 50 Tbps input bandwidth
Block synchronous data
transfer scheme …
Pt stub finding reduce the data volume by ~ 10-20,
making it possible to transfer the data out for off-detector L1 track finding

## Slide 27: CMS new Tracker Layout and Trigger Tower (6 in eta x 8 in phi)
15K modules
What we learned from FTK data formatting helps to understand CMS L1 case
Animation by Jamieson Olsen (FNAL engineer)

## Slide 28: CMS new Tracker Layout and Trigger Tower (6 in eta x 8 in phi)
15K modules
For a given stub (on a module),
how many trigger towers
need it.
What we learned from FTK data formatting helps to understand CMS L1 case

## Slide 29: CMS L1 Trigger Tower Data Sharing
In other words,
A Trigger Tower shares at most
with 8 other Trigger Towers
In fact,
Only with immediate neighbors
n
m
n
m-1
n
m+1
n-1
m
n-1
m-1
n-1
m+1
n+1
m
n+1
m+1
n+1
m-1
Eta
Phi

## Slide 30
CMS L1 tracking trigger for Phase II:
6 (in eta) x8 (in phi) = 48 Trigger towers &
their interconnections
Data coming from a given trigger
tower may need to be delivered
to multiple trigger towers.
This happens,
when a stub comes from a detector
element is close to the border
Between trigger towers, due to the
finite curvature of charged particles
in the magnetic field and finite size
of the beam luminous region
along the beam axis.

## Slide 31
φ
η
Simple
Trigger Tower
Interconnections.
Each box represents
a trigger tower.

## Slide 32
ATCA
CMS
Tracking Trigger Towers
AM or other track finding approaches implemented on mezzanine (PR engine)

## Slide 33: More advanced configuration
Ten Processors and the Gateway send the event to the target Processor Blade in a round robin scheme.
Note: animated GIF, view as slideshow in PowerPoint
The full mesh based architecture is highly flexible.
Many performance and bandwidth bottlenecks can be solved/avoided simply by better configurations.
This also makes an early technical demonstration feasible using today’s technology.
The flexible architecture is a good platform for a vertical slice demonstration and beyond.
To/from eight neighbor
towers
Each processor receives data
directly from upstream on RTM,
and then take turn to handle
different event for each trigger
tower

## Slide 34: Pattern recognition mezzanine concept
in coming
data
AM1
AM2
Group the patterns and configure the
AM Chips in such a way that
only relevant stubs/hits sent to the
relevant AMchip.
L6
L5
L4
L3
L2
L1
Associative Memory chip

## Slide 35
First Pulsar 2a prototypes work well: “plug & play” (summer 2013)
Pulsar 2b
Pulsar 2b:
  Vertex 7 FPGA (XC7VX690T)
80 GTH lines
General purpose design
I/O ~1 Tbps
Pulsar 2a
(Kintex 7 FPGAs)
http://www-ppd.fnal.gov/EEDOffice-w/Projects/ATCA/
Board delivery later this month
How
full-mesh
used for
CMS
L1 TT case

## Slide 36: Pulsar IIa Full crate testing at Fermilab
activate all the GTX at 6.25 Gb/s on 7 boards on full-mesh backplane
Hub board
Achieved maximum speed:
Local bus: 10 Gb/s
RTM : 10 Gb/s
Notes: HUB board / mezzanine card (LVDS) Pulsar Iib

## Slide 37: Comparison: ATLAS L2 FTK and CMS L1 Track Trigger
New
Tracker/Cabling
designed for
Tracking Trigger
for HL-LHC
Existing
Tracker/cabling
not designed for
Tracking Trigger
4 η x 16 φ = 64 trigger towers
6 η x 8 φ = 48 trigger towers
This leads to new Architecture….

## Slide 38
CDF SVXII
Data formatting
Pattern Recognition
Track
Fitting
Data transfer
AM system capable of dealing with the
HL-LHC collisions, with the much shorter latency
required by Level 1 triggering, poses significant
technical challenges.
(Emerging 3DIC technology can help)
HLT
Detector design for triggering
Beam spot
Silicon Based Tracking Trigger at Hadron Colliders
Partition detector into
trigger towers/sectors
Pick your favorite method:
Associative Memory (AM) Approach
(proven approach from CDF/SVT)
Finer pattern recognition

## Slide 39: 3D Technology in 30 seconds
3D technology: the integration of thinned and bonded silicon integrated circuits with vertical interconnects between IC layers
  Vertical interconnects: Through-Silicon-Vias (TSVs)
  Applications: memories, pixel arrays, microprocessors & FPGAs
Performance can be improved by reducing interconnect R/L/C for higher speed and density…
Freedom to divide functionality among tiers to create new designs that are simply not possible in 2D
  Useful when a task can be partitioned into multiple sections that are physically and logically separable, and the interconnects among them are straightforward
  Moore’s law is approaching severe limitations
  3D could be the next scaling engine
  Not just as merely an extension of Moore’s law,
  also provides novel design opportunities

## Slide 40: “A New Concept of Vertically Integrated Pattern Recognition Associative Memory” TIPP 2011 Proceedings http://www.sciencedirect.com/science/article/pii/S1875389212019165
Pattern recognition for tracking
is naturally a task in 3D
track
fired road

## Slide 41
The 3D stack is very thin ( < ~ 10 um per tier)
Directly shortens the longest of the driving lines in the
pattern recognition cell (address match lines).
 reduced power density or increased speed
VIPRAM Design philosophy (2D & 3D): implement the core of AM engine,
leave most of the control and interface logic to FPGA.

## Slide 42: Design involved
CAM cell design
Majority Logic
Cell design
Control/interface
Initial R&D goal:
Proof-of-principle demonstration
25μm
In 130nm

## Slide 43
Fig. 4 - A 3D PRAM
VIPRAM concept
In 3D, with 130 nm, VIRPAM ~160K AM patterns/cm^2
CDF AMchip03: 180 nm, standard cell, 5K AM patterns/chip
3D Architecture intrinsically open/flexible:
“CAM cell” doesn’t have to be CAM
e.g. simple algorithm or even NN …
platform to implement more advanced/fast
pattern recognition algorithm…
possible area for breakthrough

## Slide 44
3D building blocks are implemented and tested in 2D:
important design & test methodology

2D protoVIPRAM
130nm
Global Foundries
5.5mm X 5.5mm
CAM CAM CAM CAM ML
25μm
Every single transistor in the core pattern can be tested in 2D
Much of the design work
gone into optimization in 2D
VIPRAM prototyping work at Fermilab

## Slide 45
First protoVIPRAM in 2D
Chip delivered Jan 2014
Initial testing successful,
No problem found.
What’s next:
Performance scan
3D stacking …
People involved so far from Fermilab:
Engineers: G. Deptuch, J. Hoff, S. Joshi, J. Olsen, M. Trimpl,
Physicists: S. Jindariani, T. Liu, N. Tran
Power/thermal analysis by
W. Xia, P. Gui ( SMU EE)

## Slide 46
VIPRAM
test socket
Test mezzanine card
design
actual card
SVT in a mezzanine
protoVIPRAM chip
Future versions
Being used for testing new AM chips at FNAL
74 mm x 149 mm

## Slide 47
2 meters
0,1
2,3
4,5
6,7
8,9
10,11
fan-out
fan-in
SVT in one chip: 2nd phase of VIPRAM project
 general purpose pattern recognition
AM
FPGA
RAMs
AM
AM
VIPRM
Original SVT system had ~400K patterns total
Aim to reach ~500K patterns per chip for VIPRAM (long term goal)…
New 2.5/3D technology

## Slide 48
Potentially possible to directly
identify/confirm lepton objects at L1,
many advantages this way…
potential for lepton isolation on chip…
animation
After all, the main
purpose of
L1 tracker info
is to confirm
L1 muon
and electron
candidates
Associative memory
||
Confirmation memory
(Food for thoughts)

## Slide 49
One way to reformat data into VIPRAM
The concept
does not
depend on 3DIC.
Can be done in 2D.
Associative memory
||
Confirmation memory
L1 Muon tracks
L1 CAL e/γ
Potentially possible to directly
identify/confirm lepton objects at L1,
many advantages this way…
potential for lepton isolation on chip…

## Slide 50: Experiment on chip Lepton isolation in a chip?
High Pt lepton
High Pt lepton takes much less patterns
Isolation veto doesn’t require high eff for low Pt tracks much less patterns
Number of fired roads MUCH less (track fitting stage MUCH simpler/faster)
(Food for thoughts)

## Slide 51
What if one could implement
much more patterns with 3D?
Triggering Taus at L1?
Need detailed studies
tau
Experiment on chip?
(Food for thoughts)

## Slide 55
2005

## Slide 56
Data Source stage
Tracking Trigger
Vertical Slice System Demonstration
over next few years
The tracker design cannot be finalized
without demonstration of tracking trigger
one trigger tower
With the goals:
  Performance study (latency, efficiency etc)
  Identify issues/bottlenecks
  Guide future R&D, find solutions
  A common platform to explore
  new ideas/algorithm/approaches

## Slide 57: with some examples
CDF SVXII
Data formatting
Pattern Recognition
Track
Fitting
Data transfer
Emerging 3DIC
Technology promising
HLT
Detector design for triggering
Beam spot
Telecommunication technology
Tracking Trigger capability will be crucial to
the frontier physics reach at HL-LHC.
Significant improvements, or breakthroughs,
will be needed.
Aggressive R&D on going, still much challenges ahead!
Extremely fast data communication & massive pattern recognition
Technical demonstration needs to be done in a few years
Extensive simulation work for physics cases to guide the R&D
USCMS: FNAL/Northwestern/Cornell/Purdue/Florida/…(LPC)
HL-LHC Tracking Trigger Challenges
Modern FPGAs

## Slide 58: Backup slides
3DIC intro
others

## Slide 59: Some Basic TSV Information
TSV ranges in size from 1-100 um in diameter and are filled or plated with a conductive material.
TSVs are primarily used as an electrical connection or a heat conductor.
A TSV is a critical part of the 3D integration process
TSVs are used in
  3D wafer level packages
  3D silicon interposers
  3D integrated circuits
“3D packaged” parts that do not use TSVs are NOT considered 3D integration

## Slide 61: Anatomy of a PRAM (Pattern Recognition Associative Memory)
CAM Cells
(only 6 out 15 bits shown)
address
match
latch
Majority Logic
Trace Length -> Capacitance -> Power Consumption or Reduced Speed
More detector layers, or more bits involved, design more spread out in 2D
Challenges in 2D

## Slide 62
8 Data
Input
Boards
4 Pattern
Recognition
Boards
40Gbps
Commericial HUB boards
ATCA
Full-Mesh
Backplane
What’s inside
one trigger
tower/crate
One simple configuration
as an example
Fibers from upstream

## Slide 63
8 Data
Input
Boards
4 Pattern
Recognition
Boards (PRB)
Commericial HUB boards
One simple configuration
as an example
Fibers from upstream

## Slide 64
8 Data
Input
boards
4 Pattern
Recognition
Boards
Commericial HUB boards
One simple configuration
as an example
Fibers from upstream

## Slide 65
Data Input board Close-up
RTM:
Fibers
from upstream
(FPGA)
Fabric backplane
Rough estimate:
Assume 200 stubs / trigger tower, ~32 bits per stub (overestimated), the traffic from DIB to each PRB is about 8Gbps with zero suppression

## Slide 66
Pattern Recognition Board (PRB) data flow
AM based
Neighbor
data sharing
to/from
another
Trigger Tower

## Slide 67: Pattern Recognition Mezzanine (PRM)
Relaxed Performance Requirements (in the case of 10 PRBs with ~40 PRMs):
40MHz input handled by 40 PRM mezzanines in round robin, each handles
~1MHz event input rate
Event Processing >= 1MHz (out of 40MHz)
Input BW >= 16Gbps
In the case of AM approach:
~10 AM chips / PRM
~200k patterns / AMchip
~ 2M patterns / tower
(2M x 48 towers ~ 100M patterns)
The relaxed performance requirement would make
early technical demonstration easier for different
track finding approaches.
System size shrinks with better
AMchip performance:
If 2X more AM pattern density,
or 2X higher AM speed,
2 x less system size
(48 crates  24 crates)